## Slide 1
Air-Gap Orchestrator Registration and EC-S-P Licensing
Version 1.0 process deck for one self-hosted Orchestrator and three physical EdgeConnect EC-S-P appliances.
1 Orchestrator
Self-hosted deployment; Air-Gap mode is a controlled and hard-to-reverse change.
3 EC-S-P appliances
Physical EdgeConnect appliances must be licensed and then enabled for Air-Gap mode individually.
Manual exchange
Registration responses, license files, and supporting files move through approved removable-media controls.
HPE Aruba Networking EdgeConnect SD-WAN Air-Gap runbook | Do not store keys or license files in Git
01

## Slide 2
VERSION 1.0
Process at a Glance
Prepare
Portal account, versions, serials, transfer controls
>
Register
Exchange Orchestrator key and portal response
>
License
Assign EC, Boost, and feature licenses
>
Upload
Move license and supporting files to Orchestrator
>
Enable
Turn on Air-Gap mode on each EC-S-P
License and supporting files are operational artifacts, not repository artifacts.
Download a new license file after every add, reassign, or revoke action.
After file upload, appliance enablement is repeated on edgeconnect-1, edgeconnect-2, and edgeconnect-3.
HPE Aruba Networking EdgeConnect SD-WAN Air-Gap runbook | Do not store keys or license files in Git
02

## Slide 3
VERSION 1.0
Boundary Model: Connected Portal, Isolated SD-WAN
Internet-connected side
Air-Gap Portal
HPE account
License assignment
Required file downloads
Approved transfer
Removable media
Malware scan
Chain of custody
Temporary files outside Git
Isolated side
Orchestrator Air-Gap tab
License file upload
Supporting file upload
EC-S-P appliance UIs
>
registration key
>
portal response / files
Repository rule
The repo stores the runbook, scripts, and final docs only. It must not store registration keys, account keys, portal responses, license files, supporting ZIPs, or appliance backups.
HPE Aruba Networking EdgeConnect SD-WAN Air-Gap runbook | Do not store keys or license files in Git
03

## Slide 4
VERSION 1.0
Register the Orchestrator
Enable Air-Gap
Orchestrator > Orchestrator Server > Licensing > Air-Gap
Select Enable Air-Gap mode and confirm.
Copy key
Click Air-Gap Registration, Show Registration Key, then Copy Registration Key.
Portal response
Paste the key in the Air-Gap Portal Register Orchestrator tab and copy the response.
>
>
Complete registration
Return to Orchestrator > Licensing > Air-Gap, paste the portal response, click Save Portal Response, and close the dialog.
HPE Aruba Networking EdgeConnect SD-WAN Air-Gap runbook | Do not store keys or license files in Git
04

## Slide 5
VERSION 1.0
License the Three EC-S-P Appliances in the Portal
Open License & Manage Appliances and confirm all three EC-S-P serial numbers are present.
Select the appliances to license; verify the selection because the portal may default to all appliances.
Use Assign/Revoke Licenses to Add/Replace EC size, Boost, WAN Optimization, or Advanced Security / DTD.
Click Apply and verify the table shows expected licenses for edgeconnect-1, edgeconnect-2, and edgeconnect-3.
Bulk assignment
All appliances must be on the same software version.
RMA rule
Revoke an appliance license before RMA activity.
HPE Aruba Networking EdgeConnect SD-WAN Air-Gap runbook | Do not store keys or license files in Git
05

## Slide 6
VERSION 1.0
Download and Upload Required Files
Download from portal
Select all appliances, click Download Required Files, then download Appliance Licenses and Supporting File.
Transfer inward
Move both encrypted files into the isolated environment using the approved transfer process.
Upload to Orchestrator
Use Air-Gap File Upload to upload the license file and supporting file package.
>
>
Operational cadence
Download a new license file after every license change. Update the supporting file package monthly or according to HPE guidance and local policy.
HPE Aruba Networking EdgeConnect SD-WAN Air-Gap runbook | Do not store keys or license files in Git
06

## Slide 7
VERSION 1.0
Enable Air-Gap Mode on Each EC-S-P
edgeconnect-1
1. Administration > HPE Aruba Networking Cloud Services
2. Select Enable Air-Gap Mode
3. Enter Orchestrator IP
4. Administration > License & Registration
5. Enter account name and account key
6. Apply and sign out
edgeconnect-2
1. Administration > HPE Aruba Networking Cloud Services
2. Select Enable Air-Gap Mode
3. Enter Orchestrator IP
4. Administration > License & Registration
5. Enter account name and account key
6. Apply and sign out
edgeconnect-3
1. Administration > HPE Aruba Networking Cloud Services
2. Select Enable Air-Gap Mode
3. Enter Orchestrator IP
4. Administration > License & Registration
5. Enter account name and account key
6. Apply and sign out
repeat per appliance
account name is case-sensitive
serial must be in license file
HPE Aruba Networking EdgeConnect SD-WAN Air-Gap runbook | Do not store keys or license files in Git
07

## Slide 8
VERSION 1.0
Validation and Completion Criteria
Orchestrator validation
Air-Gap mode enabled
Registration complete
Latest license file uploaded
Latest supporting package uploaded
No unexpected Air-Gap alarms
Appliance validation
All three EC-S-Ps visible
Expected serial numbers
Valid EC licenses
Optional licenses present
Software versions match plan
Repo validation
Run git status --ignored
Confirm sensitive files are absent
Commit only docs, scripts, and final deliverables
Complete when Orchestrator is registered, all three EC-S-P appliances are licensed and visible, and no sensitive Air-Gap artifacts are in Git.
HPE Aruba Networking EdgeConnect SD-WAN Air-Gap runbook | Do not store keys or license files in Git
08